## Slide 1: Chapter 4
Local Area Networks
https://cis.BBent.com/Courses/CSIS202/Lessons/1
Notes: After mastering the material in this chapter you should:
1. Understand the value of the OSI Model in the analysis of network architecture
alternatives.
2. Understand how access methodologies, logical topologies, and physical
topologies combine to form alternative network architectures.
3. Understand the interaction between the various hardware and software
components of the local area network technology architecture.
4. Understand the major local area network technologies and their applications.
5. Understand basic wireless local area network technology architectures.
6. Understand how to implement, secure, and manage wireless local area networks.
7. Understand the differences between switched LAN architectures and
shared-media LAN architectures.
8. Understand the comparative differences between and proper application of
available network interface cards.
9. Understand the comparative differences between and the proper application
of hubs, concentrators, bridges, and switches.
10. Understand how proper LAN analysis can help determine which network
architecture is most appropriate in any given situation.
Access methodologies
Physical topologies
IEEE 802 standards
Ethernet
LAN hubs
Logical topologies
LAN architectures
LAN technology architectures
Wireless LANs (WiFi)
LAN switches
OSI Model
Hardware/software compatibility
Local area networks
Top-down model
Protocols and standards

## Slide 2: Layer 2: The Datalink Layer
The datalink layer provides point-to-point connectivity between devices over the physical connections provided by the underlying physical layer
The datalink layer breaks a data stream into chunks called frames, or cells.

## Slide 3: Layer 2: The Datalink Layer
The datalink layer provides a reliable communications link between devices.
Three key functions:
  error detection
  error correction
  flow control
In LANs the datalink layer can be broken down into two sublayers: media access control (MAC) and logical link control (LLC).

## Slide 4: Datalink Layer Addressing
MAC address is 48 bits long
  Equal to 12 hexadecimal digits
  1st 2 bits indentify the type of address
  Next 22 bits identify the manufacturer
  Last 24 bits are the unique serial number of the card
MAC example: 00-EO-15-9A-57-E6 (in hex)
000000001110000000010101100110100101011111100110 (in binary)
MAC addresses must be unique within each network segment

## Slide 5: Datalink Layer Addressing
Broadcast
  Send to all devices on a network segment
  Destination MAC address is all 1’s
Unicast
  Send to specific device
  Destination MAC address of receiving device
Multicast
  Send to a group of devices

## Slide 6: Datalink Layer Addressing
Promiscuous Mode
  Generally devices will ignore all messages NOT addressed specifically to their MAC address
  In order for device to receive all messages being transmitted on a network segment it must be set to “Promiscuous Mode”

## Slide 7: Datalink Layer Addressing
Frame transmitted to hub

## Slide 8: Datalink Layer Addressing
  Frame repeated by hub
  Note MAC addresses

## Slide 9: Network Segments
Least precise term
All of the devices on a local area network that can be addressed directly w/o the use of a router or other layer 3 device

## Slide 10: IP Subnet
Also referred to as just a “subnet”
A subdivision of an IP address space
May or may not map directly to a network segment in modern day switched networks

## Slide 11: Collision & Broadcast Domains
Collision Domains
  A collection of devices that share media directly
  Only one device can transmit at a time
Broadcast Domains
  The collection of devices that will hear a broadcast message sent at the DataLink layer regardless of network structure
  The use of bridges and LAN switches allow a single network segment to be broken into multiple collision domains although they remain a part of the same broadcast domain

## Slide 12: Collision & Broadcast Domains
Hub or
Multi-Port Repeater
All Computers are part of the same Collision and Broadcast domain

## Slide 13: Collision & Broadcast Domains
Switch
All computers are still part of the same broadcast domain, but now each computer is in a separate collision domain
Collision Domain
Broadcast Domain

## Slide 14: History of LAN Architectures
ALOHAnet (Univ. of Hawaii 1970)
Ethernet (Xerox 1973)
DECNet (Digital Equipment Corp. 1975)
ARCNet (Datapoint corp. 1976)
Token Ring (IBM 1985)
Local Talk (Apple 1985)
Wireless LAN/WLAN (IEEE 1991, Apple 1999)

## Slide 15: LAN Architecture Model
A network’s architecture consists of a:
  Access methodology
    CSMA/CD, CSMA/CA, Token Passing, etc.
  Logical topology
    Sequential Access or Broadcast Access
  Physical topology
    Bus, Ring, Star, Mesh
No single architecture is best in all circumstances.
Network Configuration = Architecture + Media

## Slide 16: Access Methodology
CSMA/CD
  Carrier sense multiple access w/collision detection
  Propagation Delay
    Time it takes signal from source to reach destination
CSMA/CA
  Carrier sense multiple access w/collision avoidance
Token Passing
  Device makes request to transmit and must posses the “token” before it can transmit
  Ensures transmitting device has 100% of channel

## Slide 17: CSMA/CD vs. Token Passing
CSMA/CD becomes less efficient at high bandwidth demand.

## Slide 18: Logical Topology
Method of Delivering Data
Sequential
  Data is passed from one node to the next until it reaches its destination
  Also known as a ring logical topology
Broadcast
  Data is sent to all nodes simultaneously
  Each node decides if data is addressed to it specifically

## Slide 19: Physical Topology
Ring
  Packets passed sequentially
Bus
  Linear arrangement of devices
  Terminators at both ends
  Any loose connection downs entire LAN
Star
  Used in most modern networks
  Single point of failure
Mesh
  Multiple paths between source & destination

## Slide 20: LAN Technology Model
A LAN, regardless of network architecture, requires the following components:
  A Central Wiring Concentrator
    Hub, MAU, Concentrator, or LAN Switch
  Media
  Network Interface Cards (NICs)
    Physical link between PC & media
  Network Interface Card Drivers
    Interface between NIC & Operating System (OS)
  Network OS & Applications

## Slide 21: LAN Technology Architecture

## Slide 22: LAN Technology Choices

## Slide 23: NIC Technology Analysis Grid
Servers should contain faster NICs than clients to prevent bottlenecks
NICs need to be compatible with CPU bus, chosen media, & network architecture

## Slide 24: Ethernet
  “Born” May 22, 1973
  Based on Aloha Net (Univ. of Hawaii)
Invented by Robert Metcalfe
  MIT graduate
  Developed Ethernet with Robert Boggs at Xerox’s Palo Alto Research Center (PARC)
  Founder of the 3COM company
Robert Metcalfe receiving the U.S. National Medal of Technology (2003)

## Slide 25: Ethernet
Frame-based computer networking architecture for LANs
Traditional Ethernet can be defined as follows:
  Access methodology: CSMA/CD
  Logical topology: Broadcast
  Physical topology: Historically—bus, currently—star

## Slide 26: Ethernet Standards
3 Standards:
  DIX 1.0 (Digital, Intel, Xerox)
  Ethernet II (DIX 2.0)
  IEEE 802.3/802.2

## Slide 27: Ethernet Frame Layout
802.3 length field indicates length of the variable-length 802.2 LLC data field containing all upper-layer embedded protocol headers. 802.2 info includes DSAP & SSAP.

## Slide 28: Ethernet Nomenclature
XbaseY
X=speed
Base=Baseband transmission
  One frequency, both directions
Y=media
10baseT

## Slide 29: Typical FastEthernet Architecture
Extended Star Topology
Dual Speed Hub or Switch
Autosensing Ports

## Slide 30: Gigabit Ethernet
Also known as 1000BaseX, is an upgrade to fast Ethernet that was standardized as IEEE 802.3z :
  1000BaseSX: uses short wavelength laser multimode fiber optic media, primarily for horizontal building cabling.
  1000BaseLX: uses long wavelength laser single mode fiber optic media, primarily for high-speed campus backbone applications.
  1000BaseTX: uses four pair of CAT 5e UTP with a maximum distance of 100 m.

## Slide 31: Token Ring
Access methodology: Token passing
Logical Topology: Sequential
Physical Topology: Star
IEEE 802.5
Once contended with 802.3
New installations are uncommon

## Slide 32: ATM on the LAN
Asynchromnous Transfer Mode
  Switched technology originally developed for WANs
ATM LAN Emulation (LANE)
  LANE required for mixed environments
  MAC addresses must be translated into ATM addresses

## Slide 33: Wireless LANs
IEEE 802.11 standard
CSMA/CD at MAC layer
802.11 frames are similar to 802.3 Ethernet frames

## Slide 34: Wireless LANs – 802.11b
11 Mbps theoretical, 4 Mbps practical
2.4 Ghz band – subject to interference from common electronic equipment
Shared access – sensitive to number of simultaneous users
Commonly available, inexpensive
Range is measured in 100’s of feet, lower indoors.

## Slide 35: Wireless LANs – 802.11g
Interoperates with, similar to 802.11b
54 Mbps theoretical
Same band
Similar range
Also very common, inexpensive
802.11n – 600 Mbps theoretical (in draft stage)

## Slide 36: Wireless LANs
Care must be taken in wireless LAN designs

## Slide 37: Wireless LANs
Wireless access points can provide for client access or provide a bridge

## Slide 38: Wireless LANs
A wireless client will access the stronger channel

## Slide 39: OSI Layers 1 and 2

## Slide 40: LAN Interconnection Hardware
Many stand-alone hubs may be cascaded
5-4-3 Rule
Stackable Hubs
Stand-alone Hubs

## Slide 41: LAN Interconnection Hardware
Enterprise hubs have modular design

## Slide 42: Hub Functional Comparison

## Slide 43: Network Management
SNMP is used to manage network devices

## Slide 44: LAN Interconnection Hardware
A LAN Switch

## Slide 45: LAN Interconnection Hardware
Shared media – a “party line”
Fixed bandwidth shared by all stations

## Slide 46: LAN Interconnection Hardware
Multiple, simultaneous connections at the same rate

## Slide 47: LAN Interconnection Hardware
LAN switches use Datalink (MAC) addresses

## Slide 48: Switching
Switching is a datalink layer process, making forwarding decisions based on the contents of layer two frame addresses
Switches are transparent devices, receiving every frame broadcast on a port

## Slide 49: Switching
A switch checks the source address of each frame it receives and adds that source address to the local address table (LAT) for the port.
The switch is learning, without having to be manually reconfigured, about new workstations that might have been added to the network.

## Slide 50: Store and Forward Switching
The entire frame is read into switch memory.
Bad frames are not forwarded.

## Slide 51: Cut-through Switching
Only the address information in the header is read before beginning processing.
Very fast
Bad frames are forwarded.

## Slide 52: Error-free Cut-through Switching
Aka “Adaptive Switching”
Automatically selects best switching method for each port

## Slide 53: Advantages of Using Switches
Switches can be used to segment networks to improve performance